## Slide 1: STRING INSTRUCTIONS

## Slide 2
• movs (move string)
• lods (load string element into the accumulator)
• stos (store accumulator into string element)
• scas (Scan string and check for match against the value in the accumulator)
• cmps (compare two strings)
You can use the movs, stos, scas, cmps, instructions to manipulate a single element (byte, word, or double word) in a string, or to process an entire string.
Generally, you would only use the lods instruction to manipulate a single item at a time. These instructions can operate on strings of bytes, words, or double words.
To specify the object size, simply append a b, w, or d to the end of the instruction’s mnemonic, i.e., lodsb, movsw, cmpsd, etc. Of course, the double word forms are only available on 80386 and later procs.

## Slide 3: PREFIXES
• rep (repeat a string operation)
• repz (repeat while zero)
• repe (repeat while equal)
• repnz (repeat while not zero)
• repne (repeat while not equal
One instruction LOOP as long as CX not equal to zero

## Slide 4: MOVS{B|W|D}
movs{b,w,d}: es:[di] := ds:[si]
if direction_flag = 0
then si := si + size; di := di + size;
else si := si - size; di := di - size;
endif;
Note: size is one for bytes, two for words, and four for dwords
MOVSB, MOVSW, MOVSD

## Slide 5: CMPS{B,W,D}
The cmps instruction compares the byte, word, or dword at location ds:si to es:di and sets the processor flags accordingly.
After the comparison, cmps increments or decrements si and di by one, two, or four depending on the size of the instruction and the status of the direction flag in the flags register. cmps{b,w,d}: cmp ds:[si], es:[di]
if direction_flag = 0
then si := si + size; di := di + size;
else si := si - size; di := di - size;
endif;

## Slide 6: LODS{B,W,D}
lods{b,w,d}: eax/ax/al := ds:[si]
if direction_flag = 0
then si := si + size;
else si := si - size;
endif;

## Slide 7: STOS{B,W,D}
stos{b,w,d}: es:[di] := eax/ax/al
if direction_flag = 0
then di := di + size;
else di := di - size;
endif;

## Slide 8: SCAS{B,W,D}
scas{b,w,d}: cmp eax/ax/al, es:[di]
if direction_flag = 0
then di := di + size;
else di := di - size;
endif;