## Slide 1: Math Coprocessor
Also called Floating Point Unit
FPU

## Slide 2: Outline
Math Coprocessor Operation
Math Coprocessor Structure
Data Types
Representation error
Instructions

## Slide 3: Math Coprocessor Operation
Shares the same Data, Address and Control BUS as the main processor
Two different chips for old processors
On the same silicon die starting with 486DX
Instructions preceded by an ESC sequence
Operates in parallel with main processor
Coprocessor may overtake BUS for longer periods if more data is needed

## Slide 4: Math Coprocessor Operation
Coprocessor has no access to registers
But can use registers for addressing
All addressing modes are available except immediate addressing
Uses special synchronization signals to cooperate
Instructions take tens to hundreds of cycles to complete

## Slide 5: Math Coprocessor Structure
Register Stack
Control Register
Status Register
Tag Register
Instruction Pointer
Data Pointer

## Slide 6: FPU Register Stack

## Slide 7: FPU Control Register

## Slide 8: FPU Status Register

## Slide 9: Meaning of C3C2C1C0 bits after compare instructions
No Conditional Jumps to test FPU compare results
Must copy Status Register in to registers and examine with x86 instructions

## Slide 10: FPU Tag Register
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
TAG7 |  | TAG6 |  | TAG5 |  | TAG4 |  | TAG3 |  | TAG2 |  | TAG1 |  | TAG2 | 
TAG Values | meaning
00 | Valid
01 | Zero
10 | Special, NAN,∞
11 | Empty

## Slide 11: FPU Pointers
Instruction Pointer a pointer to the instruction that caused an exception
Data Pointer a pointer to the data used by the instruction that caused an exception

## Slide 12: Number Representation
Integer numbers in C2
Integer numbers in Packed Decimal
Real Numbers in IEEE 754/854 standard format
All these representations are ONLY in memory
Internally ALL numbers are represented on 80 bits as temporary real’s

## Slide 13: Integer Data Types
Word Integer DW 16 bit C2 representation
Short Integer DD 32 bit C2 representation
Long Integer DQ 64 bit C2 representation
Packed Decimal DT 80 bit Value & Sign

## Slide 14: Real Number Representation Normalized Form
(-1)S * 1.mantissa *2 (exponent- Bias)
Bias = 07FH for short real;127d
Bias = 03FFH for long real;1023d
Bias = 03FFFh for temp real; 16383d

## Slide 15: Short Real 32 bits Double Word DD

## Slide 16: Long Real 64 bits Quad Word DQ

## Slide 17: Temporary Real 80 bits Ten word DT

## Slide 18: Example of real number representation
fl1 dd 1.0
0000 3F800000
0011 1111 1000 0000 0000 0000 0000 0000
Fl2 dd 2.0
0004 40000000
0100 0000 0000 0000 0000 0000 0000 0000
fl1_3 dd -1.3; actually -1,299995
0008 BFA66666
1011 1111 1010 0110 0110 0110 0110 0110

## Slide 19: Representation error
Unavoidable
May be very small
Must take account when designing numerical algorithm for complex computation
Can be controlled with rounding policy from Control Word

## Slide 20: FPU Instructions
Data movement
Data conversions
Arithmetic Instructions
Comparison Instructions
Constant Instructions
Transcendental Instructions
Miscellaneous Instructions